## Slide 1: Trackers and Gain Corrections Sam Grant g-2 Collaboration Meeting (Elba): Early Career Session 28th May 2019

## Slide 2
Trackers!
Layers of wire under high voltage, encased in straws filled with an argon-ethane gas mix
Provides information about track momentum and position
Two sets of 8 modules, in front of calorimeters 13 and 19.
Very useful for studying systematics as well!
Ionisation -> Charges drift to wires -> Read out and reconstruct -> No worries

## Slide 3
Gain sag!
Sudden drop and subsequent recovery in gain at early times
This is due to bunching after injection saturating the calorimeters
Must be fitted and corrected in processing
Amplitude p1 and time constant p2 are used for gain corrections

## Slide 4
Tracker-calo matched tracks provide a different way to measure gain, so we can perform an independent cross check of the laser.
Gain = measured energy / true energy
E = p, and trackers do not “see” gain sag, so:
Gain = cluster energy (calo) / track momentum (tracker) = E/p
The E/p ratio

## Slide 5
Tracker-calo matched tracks provide a different way to measure gain, so we can perform an independent cross check of the laser.
“Just plot E/p vs time for each calo, and fit a function to it to get the amplitude and recovery time”
The E/p ratio

## Slide 6
NOT SO FAST!
🤔

## Slide 7
First up, pick a good region in E over p

## Slide 8
E/p normalisation by crystal
We can mitigate variation in E/p by normalising each crystal to it’s mean E/p (after 60 μs!)
(Gaussian means of each bin)

## Slide 9
Also, breakout boards
Two different supply circuits – we can’t combine crystals on different boards as they also have different recovery time constants!
Longer lifetime, shorter lifetime

## Slide 10
Draw normalised 2D plots
Slice vertically and fit the Y projections
Separate boards and draw gaussian means and fit exponential
Now we can get some parameters!
1.
2.
3.

## Slide 11
Now we can get some parameters!

## Slide 12
Results, by breakout board
It works for calo 13
Difficulty resolving calo 19, it’s further from injection (so less sensitive to gain sag)

## Slide 13
Change tack: crystal by crystal
The laser system records 𝛕 and A for every crystal
I’m limited by stats here, but fitting crystal by crystal allows for a direct comparison

## Slide 14
E/p fits crystal by crystal, compared with laser results

## Slide 15
“Pull” of E/p fits and laser results
Vast majority of crystals are within 3 sigma (one exception 🤨)

## Slide 16
Gain corrections, summary
Confirmation that gain sag is a real effect and not some quirk of the laser
I claim that the results used for gain corrections, as measured by the laser system, are consistent with mine
Main point: you can trust the corrections applied to remove the gain sag

## Slide 17
Thanks!

## Slide 18: BACKUP

## Slide 19
First up, E/p normalisation
We can mitigate variation in E/p by normalising each crystal to it’s mean E/p (after 60 μs!)
(Gaussian means of each bin)

## Slide 20
Lost muons!
Where are we?!
μ+
μ+
μ+
μ+
Sometimes muons exit the ring due to small perturbations in their orbit
They are a problem if you want to use the trackers: trackers can’t make an energy cut as the calos do

## Slide 21
Lost muons!
Where are we?!
μ+
μ+
μ+
μ+
“How do lost muons affect beam position measurements?”
Sometimes muons exit the ring due to small perturbations in their orbit
They are a problem if you want to use the trackers: trackers can’t make an energy cut as the calos do

## Slide 22
Lost muons, selection
μ+
μ+
μ+
μ+
μ+
μ+
  If you know energy AND momentum, you can find your lost muons:
  Momentum > 2300 MeV, -3.2 < log(E/p) < -2.4

## Slide 23
Lost muons, method
Take tracker only data as “all tracks”
Scale up lost muon population according to the relative efficiency of the calo
Subtract scaled lost muons from ”all tracks”
Have a look at how radial and vertical positions have changed

## Slide 24
Scaling the lost muons

## Slide 25
Lost muons!
Interesting tails, let’s cut at +/- 60 mm from the magic radius to get rid of them

## Slide 26
Lost muons, results!