## Slide 1: Independent check of gain corrections based on E/p vs time Sam Grant (ωa Europa) 17th May 2019

## Slide 2
Gain sag
Credit: ωa Europa
https://gm2-docdb.fnal.gov/cgi-bin/private/ShowDocument?docid=17009
Just after injection there is a slight drop and subsequent recovery of gain, which must then be corrected!
We can double check the results from the laser, and hence the gain corrections, by using tracker-calo matched tracks.

## Slide 3
Tracker-calo matched tracks provide a different way to measure gain.
The trackers measure the track curvature to get momentum, p, which is not affected by the flash
The calorimeter give the cluster energy, E, of the same track
Particles are relativistic, so E=p
E/p is therefore equivalent to gain
E/p ratio

## Slide 4
Make 2D plots of E/p vs t
Fit y-projections of each x-bin with gaussians, and plot the gaussian mean and it’s error (a better alternative to a profile)
Separate tracks according to breaker board
Require 1 crystal hit per track
Fit resulting distribution to extract the recovery time and gain sag amplitude with function:
Repeat process on a crystal by crystal basis
Compare with laser results
Method

## Slide 5
Details!
Using Europa Ntuples, available in:
gm2/data/g2be/Production/Trees/v9_17_01/60hr/
Tracker group’s quality flag: “Track quality = true”. See James Mott (2019):
https://gm2-docdb.fnal.gov/cgi-bin/private/ShowDocument?docid=16444
Cluster track time difference between -8 and +3 ns for station 12, and between -9 and +1 ns for station 18
Radial difference, dR < 30 mm
Positron selection:
  -0.3 < Log(E/p) < 0.2;
  Region of highest flux:
  1.2< E [GeV] < 2.4

## Slide 6
Breaker Boards
Short Life Times (by crystal), xtalShort[22]= {0, 9, 10, 11, 14, 15, 18, 19, 20, 23, 24, 27, 30, 31, 34, 35, 36, 39, 40, 43, 44, 45}
See Jason Hempstead (2018):
https://gm2-docdb.fnal.gov/cgi-bin/private/ShowDocument?docid=12263&version=1
Different breaker boards mean different recovery times, when combining crystals it is important to only combine those connected to the same board

## Slide 7
E/p normalisation at time > 60 μs
Different crystals have different mean values of E/p.
Find the gaussian mean E/p per crystal, after 60 μs
Normalise E/p crystal by crystal using these values
Gauss fits in backup

## Slide 8
E/p vs time, separated by breaker board

## Slide 9
Tables of recovery times, > 60% fractional energy
Also increased the fractional energy cut to > 99%. This makes almost no difference, and so I think > 60% is OK, and gives more stats!

## Slide 10
Recovery times, crystal by crystal
You could imagine with higher stats these distributions looking the same...

## Slide 11
Results from crystal by crystal fits (top), compared with results from the laser system (bottom)

## Slide 12
Conclusion
Work in progress!
Confirmation that we can see gain sag with the E/p ratio on a subset of crystals for calos 13 and 19.
Preliminary values of amplitude and recovery time are compatible with those observed with the laser
Planning on performing a side-by-side analysis with gain corrected ntuples when they become available
Working with Nandita Raha to cross check E/p means with MIP peaks.

## Slide 13: BACKUP

## Slide 14
Gauss fits – E/p means per crystal
Xtal 0
Xtal 9
Xtal 45
St 13
St 19

## Slide 15
Recovery times per station, > 99% fractional energy

## Slide 16
Tables of recovery times, > 99% fractional energy

## Slide 17
Time difference (dt), radial difference (dR), log(E/p)
Credit: Gavin Hesketh