## Slide 1: Gain correction with the E/p ratio Muons Meeting Sam Grant 17th May 2019

## Slide 2
Quick note on the g-2 detectors
24 calorimeters, 54 lead fluoride scintillating crystals in each
I am interested in calos 13 and number 19, which have 8 straw tracking detectors in front (so we can match tracks)

## Slide 3
Gain sag
Credit: ωa Europa
https://gm2-docdb.fnal.gov/cgi-bin/private/ShowDocument?docid=17009
Just after injection there is a slight drop and subsequent recovery of gain, which must then be corrected!
There is a laser system that We can double check the results from the laser, and hence the gain corrections, by using tracker-calo matched tracks.

## Slide 4
Tracker-calo matched tracks provide a different way to measure gain.
The trackers measure the track curvature to get momentum, p, which is not affected by the flash
The calorimeter give the cluster energy, E, of the same track
Particles are relativistic, so E=p
E/p is therefore equivalent to gain
E/p ratio

## Slide 5
First Step: Normalisation per crystal
Different crystals have different mean values of E/p, to consider more than one crystal at a time this must be normalised

## Slide 6
Gauss fits – E/p means per crystal
Xtal 0
Xtal 9
Xtal 45
Calo 13
Calo 19

## Slide 7
Breaker Boards
Orange crystals represent the crystals attached to the board with a shorter recovery time
Two different supply boards (breaker boards) per calo. Different electronics mean different recovery times for the crystals connected to these boards
45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53
36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44
27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35
18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8

## Slide 8
Breaker Boards
”Short lifetime”
”Long lifetime”

## Slide 9
Draw normalised 2D plots
Slice vertically and fit the Y projections
Separate boards and draw gaussian means and fit exponential

## Slide 10
Next step: do this crystal by crystal and compared with laser results

## Slide 11
Scatter plots: E/p results and laser results
E/p ratio:
Laser:

## Slide 12
2D plots: E/p results and laser results
E/p ratio:
Laser:

## Slide 13
Differences between laser and E/p results
Mean difference = 0.00529655
Mean difference = 0.0142067
Mean difference = 4.18167 us
Mean difference = 5.11914 us

## Slide 14
Summary
I still have a bit of work to do here, but I hope to tie up the loose ends pretty quickly (this week really)
The effect is real, and confirms what the laser reports.
I’m ultimately limited by stats

## Slide 15: BACKUP

## Slide 16
Make 2D plots of E/p vs t
Fit y-projections of each x-bin with gaussians, and plot the gaussian mean and it’s error (a better alternative to a profile)
Separate tracks according to breaker board
Require 1 crystal hit per track
Fit resulting distribution to extract the recovery time and gain sag amplitude with function:
Repeat process on a crystal by crystal basis
Compare with laser results
Method

## Slide 17
Details!
Using Europa Ntuples, available in:
gm2/data/g2be/Production/Trees/v9_17_01/60hr/
Tracker group’s quality flag: “Track quality = true”. See James Mott (2019):
https://gm2-docdb.fnal.gov/cgi-bin/private/ShowDocument?docid=16444
Cluster track time difference between -8 and +3 ns for station 12, and between -9 and +1 ns for station 18
Radial difference, dR < 30 mm
Positron selection:
  -0.3 < Log(E/p) < 0.2;
  Region of highest flux:
  1.2< E [GeV] < 2.4

## Slide 18
Recovery times per station, > 99% fractional energy

## Slide 19
Time difference (dt), radial difference (dR), log(E/p)
Credit: Gavin Hesketh

## Slide 20
Preamble
I am using the tau and amplitude values contained in the fcl file:
“gm2Dev_v9_20_00/srcs/gm2calo/fcl/inFillGainParams_withlognstdp.fcl”
If anyone wants my values, I have them in both csv and ROOT format
Question: why no uncertainties in the fcl file?
*Detail on cuts ect in backup

## Slide 21
E/p vs time, separated by breaker board